## Slide 1
Step 5: Gridstream Analytics
Smart Meters
E350 Residential
E360 Advanced
S4x/E650 C&I
E660/Revelo IoT
Communication Network
RF Mesh
PLC
Cellular LTE
Gridstream HES
[(Head-End System)]
Data Collection
Meter Inventory
raw readings
raw data →
Core MDMS
[(Meter Data Mgmt)]
Validation
Estimation
Editing
validated data →
Gridstream Analytics
Demand Analysis
[Peak / Avg / Min demand]
Load factor Time-of-use profiles
Voltage Monitoring
[ANSI C84.1 Range A]
±5% of nominal Exceedance counts
Revenue Protection
[Tamper detection]
Reverse flow alerts Consumption anomalies
Client Applications
REST API
[(FastAPI + OpenAPI 3.1)]
/meters
/readings
/usage-points
/analytics
/delivery-promises